## Slide 1: SyncWatch Another True Story

## Slide 2: Once Upon a Time in the North…
Scandinavian mobile operator moving to Ethernet mobile backhaul
  New backhaul network interfacing with DWDM core
  Backhaul equipment vendor already selected
  2G / 3G Base stations in current install base require sync
  Platform for LTE and future technologies
TDM sync chain to be broken as migration occurs
  FDD mode used to communicate with mobile devices
  Stable frequency required as reference to base stations
  Stability required = 16ppb (long term)
Considering options:
  Symmetricom Grandmaster & TP500 clients… or…
  IEEE 1588 solution built in to backhaul network equipment….
….Which option is the right one to use???
?

## Slide 3: Setting up the Test Environment
????
????
Engineering test bed constructed
  Two sites selected for packet clock trials
  SSU2K, Master Packet Clocks, Clients
  Max 6 Ethernet & 2 µwave hops between master & client
Embedded packet clock solution provisioned by vendor
Purchased TP5000 & multiple TP500’s from Chronos for evaluation
  Chronos to commission and ensure correct operation
TP500
SSU2K
TP5000 PTP GM
Master Clock
Embedded Client
Native Eth. Radio

## Slide 4: What do I Need to Test?
Initial setup of TP5000 & TP500
  Ensure all is installed and working correctly
  Initial indicators of performance in environment
Suitability of the network & PDV characterisation
  Effects of changing QoS/CoS or bandwidth settings, etc. can be seen immediately – May take time to show effect in clients with OXCO
  Effects of traffic loading, important
  Hard data to go back to developers if problems occur
Frequency stability at base station inputs (TP500 & Embedded)
  Ultimately, this is what matters
  Base stations had E1/2.048 MHz input for sync
    G.823 Sync + 16ppb requirement – ‘a non-standards based “standard”’
  Effects of changes to network PDV
  Long term stability over weeks of normal operation
How does SyncWatch help the above?

## Slide 5: The 2230 probe – Connections Used
GPRS Antenna
GNSS Antenna (e.g. GPS)
C: E1/T1
E: Freq, 50 ohm
G: Ethernet
RS-232/Craft I/F
DC (-48VDC)
B: 64kHz-200MHz
50 ohm/High Z
A: E1/T1
D: 64kHz-200MHz
50 ohm/High Z
Dry Relays
USB
F: 1PPS
Aux output
Mgmt Ethernet
Sync
inputs
Sync
output

## Slide 6: Provisioning PTP Solutions
SyncWatch Standalone mode
Real time data / analysis
  Live TIE / MTIE / TDEV
One to one tool with laptop
Live reporting of results for immediate interpretation
Easy to deploy GPS antenna
AUX Out provides PRC reference to PDV tester – extremely handy!
TimeMonitor Analyzer also useful for PDV data analysis
TimeMonitor
Software
Sync performance data streamed live to TimeMonitor application
Probe
GPS
PDV Tester
Aux Out
TP500
Embedded Client

## Slide 7: Standalone Testing
Live phase data displayed as it is received from probe
Simple set-up, connect then hit ‘Start’
Enter view mode to see MTIE/TDEV while still collecting data from probe
Phase plots can be imported into TimeMonitor Analyze for full mask based analysis
Phase / MTIE / TDEV View On The Fly

## Slide 8: PTP Client Evaluation Setup
TP500
E1 Out
SSU2K
GPS
TP5000 GM
Master Clock
Test Environment
TP5000 and other Master Clock locked to SSU2K
3x Network hops until microwave
2x Microwave hops then multi-service switch
E1’s monitored at both PTP clients, reference is GPS
Native Ethernet Radio
2x Hops Max
Embedded Client
E1 Out
Multi-Service Switch
Core Infrastructure

## Slide 9: Long term monitoring of performance
SyncWatch Managed mode
One to many system
  Single server aggregates all sites data
  Two sites in this trial – 100s possible
Monitoring and Alerting
  Relevant ‘exception’ masks defined
  If mask broke, could correlate this back to network events
Long term performance now being logged
Compared performance of TP500 and Embedded clients
Integrated with SNMP management system for alert reporting
External reference
Server
SNMP
Probe
Fixed & µwave
Network
TimeMonitor
Software
Probe
Probe
Probe
Probe
GPS
GPS
GPS

## Slide 10: Server / Client Mode
Server holds performance data for all sites in the trial
Customer evaluated both solutions over 1 month
Normal and exceptional traffic conditions
Used SyncWatch graphs in their final report
Phase data for broken masks

## Slide 11: Chronos / Symmetricom Test Results
TP500 client performed to a high standard, with MTIE well inside G.823 and 16ppb masks.
TP5000 was also evaluated and the customer liked the product
Plot below taken from Chronos commissioning test, 2 microwave hops
MTIE Plot – TP500 – 4 Hour Commissioning Test

## Slide 12: Who was Left Out in the Cold?
TP500 outperformed Embedded client under normal operation
  Even though embedded solution employed transparent clocks at every node
Customer decided to go with Embedded Client solution, mainly based on cost, however….
… They were impressed with the TP5000 and wanted to keep sync master separate from traffic, looking to deploy multiple TP5000’s
  Waiting for v1.2 release as this supports multicast PTP
Customer realised the importance of permanent monitoring
  Ordered 15x SyncWatch Probe, SyncWatch Server & SNMP option
  SyncWatch written in to deployment guidelines and to be installed at newly migrated sites in every region
  ‘Worst case’ sites selected – most radio hops from grandmaster
  G.823 + 16ppb masks configured on SyncWatch Server – alarms forwarded to NOC if exception occurs
  Pool of SyncWatch probes kept in central location to be used for emergency or ad-hoc testing

## Slide 13: SyncWatch Monitoring in all Environments